## Heavy Duty Gap Bed Lathes Specifications

|  | GT-2060 | GT-2080 |
| --- | --- | --- |
| Max. swing over bed | 20” |
| Max. length of workpiece | 60” | 80” |
| Max. swing over cross slide | 12” |
| Max. Swing in gap | 28” |
| Width of Bed | 15-1/2” |
| Effective length in gap to spindle | 9” |
| Effective length in gap to chuck jaws | 6” |
| Spindle bore | D1-8 . 4-1/8” |
| Taper of spindle center | MT6 |
| Spindle speeds | 36-1,600 rpm / 12 steps |
| Longitudinal feeds | 0.0023-0.093 IPR, 65 kinds |
| Cross feeds | 0.0011-0.04 IPR, 65 kinds |
| Inch threads | 28-2 TPI, 25 kinds |
| Metric threads | 1-14 mm , 22 kinds |
| Module threads | 0.5-7 mm, 18 kinds |
| Diameter pitch threads | 56-4 DP , 24 kinds |
| Max. travel of top slide | 5-3/4” |
| Max. travel of cross slide | 12-1/2” |
| Longitudinal rapid traverse | 18 ft / min. |
| Cross rapid traverse | 8 ft / min. |
| Diameter of tailstock quill | 3” |
| Max. travel of tailstock quill | 6” |
| Taper of tailstock quill center | M.T. # 5 |
| Max. weight of workpiece | 2000 LBS |
| 4-way tool post size | 1” x 1” |
| Longitudinal leadscrew diameter / pitch | Diameter: 3” Pitch: 2 TPI |
| Main Motor | 10 HP, 220V/440V, 3p hase, prewired on 220V |
| Rapid traverse motor | 1/3 HP, 220V/440V, 3 phase, prewired on 220V |
| Coolant pump motor | 1/8 HP,220V/440V, 3 phase, prewired on 220V |
| Net weight, approx. | 8,100 LBS | 8,300 LBS |
| Overall dimensions, LxWxH | 106” x 43” x 53” | 123” x 43” x 53” |